## Slide 1
LAB 1 – ALU and Tool Introduction
IAS0630 Hardware Security SPRING, 2026.
Sharjeel Imtiaz Email: sharjeel.imtiaz@taltech.ee
Centre for Dependable Computing Systems
Dpt. of Computer Systems - School of IT
Tallinn University of Technology
Notes: Started in dec.

## Slide 2: Lab 1 Overview
Objectives:
  Become familiar with the Linux-based lab environment
  Learn how to compile and simulate Verilog designs
  Use Xcelium simulator and waveform viewer
  Implement a simple ALU in Verilog
Tools Used:
  Linux Terminal
  Cadence Xcelium (xrun)
  Verilog HDL
Required Environment:
  Linux OS (lab PCs are dual-boot)
  TalTech credentials for login
  Terminal access
Important Notes:
  If the machine boots into Windows, restart and select Linux
  All work should be done inside your home directory
All Lab Files
  Index of /~spagliar/teaching/ias0630/labs

## Slide 3: Basic Linux Setup
Open a terminal and type.
  cd ~
  mkdir work
  cd work
Load Cadence tools:
  Type Cad
  Select option 1 – Cadence
Download sample design:
  wget https://ati.ttu.ee/~spagliar/teaching/ias0630/labs/sample.v
Run simulation:
  xrun sample.v
Expected Output:
  IAS0630 FSM SAMPLE
  Simulation complete via finish.
Simulate with GUI:
  xrun -gui -debug sample.v
You should observe:
  A waveform window &A counter counting from 32 down to 0

## Slide 4: ALU Lab Description
Task:
  Design a combinational ALU using Verilog.
ALU Features:
  3 operands (8-bit each)
  3 operations
    ADD: add 2 inputs
    SUB: subtract 2 inputs
    ATS: add 2 inputs, sub the third
  Controlled using opcode and enable signals.

## Slide 5: ALU Lab Description
Inputs:
  operand_a, operand_b, operand_c (8-bit)
  use_a, use_b, use_c (operand enable signals)
  opcode_add
  opcode_sub
  opcode_ats (add then subtract)
Outputs:
  result (8-bit)
  error (1-bit)

## Slide 6: Operation Rules (Very Important)
Exactly one opcode must be active at a time.
Operand requirements:
  ADD → exactly 2 operands enabled
  SUB → exactly 2 operands enabled
  ATS → exactly 3 operands enabled
If rules are violated → error = 1
Error triggers when the number of used inputs does not match the number of operators for the given opcode.
A testbench is provided in lab1_tb.v for your reference; you can modify it accordingly.

## Slide 7: Deliverables
Submit in zip files and the name of the zip file should be
  Lab1_StudentID.zip
Zip file should contain.
  Verilog module file (lab1.v)
  Screenshot of successful simulation
  Waveform screenshot showing correct behavior
  A brief working flow of ALU design in your observation.

## Slide 8
Thank you!