## Slide 1
LAB 2 – Router Design
IAS0630 Hardware Security SPRING, 2026.
Sharjeel Imtiaz Email: sharjeel.imtiaz@taltech.ee
Centre for Dependable Computing Systems
Dpt. of Computer Systems - School of IT
Tallinn University of Technology
Notes: Started in dec.

## Slide 2: Lab 2 Overview
Objectives:
  Understand packet-based data transfer on a fixed-width bus
  Implement a simple router using sequential logic
  Accumulate and forward packets based on protocol rules
  Analyze timing behavior using simulation and waveforms
Tools Used:
  Linux Terminal
  Cadence Xcelium (xrun)
  Verilog HDL
Required Environment:
  Linux OS (lab PCs are dual-boot)
  TalTech credentials for login
  Terminal access
Important Notes:
  If the machine boots into Windows, restart and select Linux
  All work should be done inside your home directory
All Lab Files
  Index of /~spagliar/teaching/ias0630/labs

## Slide 3: Basic Linux Setup
Open a terminal and type.
  cd ~
  mkdir work
  cd work
Load Cadence tools:
  Type Cad
  Select option 1 – Cadence
Download sample design:
  wget https://ati.ttu.ee/~spagliar/teaching/ias0630/labs/sample.v
Run simulation:
  xrun sample.v
Expected Output:
  IAS0630 FSM SAMPLE
  Simulation complete via finish.
Simulate with GUI:
  xrun -gui -debug sample.v
You should observe:
  A waveform window &A counter counting from 32 down to 0

## Slide 4: Lab Description
Task:
  Design a router module that receives packets over a 32-bit input bus, reconstructs the packet internally, and forwards it according to given constraints.
Router Features:
  Packet size: 96 bits
  Input/output bus width: 32 bits
  Packets transferred in 4 cycles in, 4 cycles out
  Sequential design using clocked logic
Packet Structure
Important:
  Packets travel on a 32-bit bus
  You must accumulate incoming data before transmission
  Check lab2_tb.v to understand exact bit ordering

## Slide 5: Functional & Timing Constraints
valid_i must be asserted one clock cycle before valid data
valid_i must be deasserted with the last data word
Total operation time: 8 clock cycles
  4 cycles for receiving
  4 cycles for transmitting
No idle cycles between receive and transmit
Implementation Constraints:
  Use one 96-bit internal register
  Use one 3-bit counter
  Use two always @(posedge clk) blocks

## Slide 6: Expected waveform

## Slide 7: Routing Rules & Packet Filtering
Packet Handling Rules:
  Increment hops by 1 for every transmitted packet
  Do not forward packet if:
    Header ≠ 3’b101
    Tail ≠ 3’b010
    Hops > 6’d10
Additional Requirements:
  Use a third always @(*) block
  Print a message on the terminal when a packet is dropped
  Message must appear in the same cycle the condition is detected
Verification
  Use waveform viewer to verify:
    Counter operation
    Packet accumulation
    Output timing and validity signals
  Expected waveform is provided
  Refer to lab2_tb.v to understand stimulus behavior

## Slide 8: Deliverables
Submit a zip file named:
  Lab2_StudentID.zip
Zip file should contain.
  Verilog module file (lab2.v)
  Screenshot of successful simulation
  Waveform screenshot showing correct behavior
  Brief description of router working flow (in your own words)

## Slide 9
Thank you!