## Slide 1
LAB 3 – Finite State Machines (FSM)
IAS0630 Hardware Security SPRING, 2026.
Sharjeel Imtiaz Email: sharjeel.imtiaz@taltech.ee
Centre for Dependable Computing Systems
Dpt. of Computer Systems - School of IT
Tallinn University of Technology
Notes: Started in dec.

## Slide 2: Lab 3 Overview
Objectives:
  Understand and implement Finite State Machines (FSMs) in Verilog
  Design a sequential hash function using FSM-based control
  Handle overflow conditions using state transitions
  Verify FSM behavior using simulation and waveform analysis
Tools Used:
  Linux Terminal
  Cadence Xcelium (xrun)
  Verilog HDL
Required Environment:
  Linux OS (lab PCs are dual-boot)
  TalTech credentials for login
  Terminal access
Important Notes:
  If the machine boots into Windows, restart and select Linux
  All work should be done inside your home directory
All Lab Files
  Index of /~spagliar/teaching/ias0630/labs

## Slide 3: Basic Linux Setup
Open a terminal and type.
  cd ~
  mkdir work
  cd work
Load Cadence tools:
  Type Cad
  Select option 1 – Cadence
Download sample design:
  wget https://ati.ttu.ee/~spagliar/teaching/ias0630/labs/sample.v
Run simulation:
  xrun sample.v
Expected Output:
  IAS0630 FSM SAMPLE
  Simulation complete via finish.
Simulate with GUI:
  xrun -gui -debug sample.v
You should observe:
  A waveform window &A counter counting from 32 down to 0

## Slide 4: Lab Description
Task:
  Design an FSM-based circuit that computes a simple hash function over sequential input data.
Hash Function:
  Used for signature generation or reduction
  Fix operation:
    hash = (hash mod 997) + 7
A testbench is provided in lab3_tb.v

## Slide 5: Inputs and Outputs
Inputs:
  clk – system clock
  rst_n – asynchronous active-low reset
  use_seed – selects initial hash value
  data_i (8-bit) – input data
  valid_i – indicates valid input data
Outputs:
  data_o – hash output
  valid_o – indicates valid hash output
Initial Hash Value:
  333 if use_seed = 1
  0 if use_seed = 0

## Slide 6: FSM Functional Rules
On every clock cycle:
  If valid_i = 1, input data is processed
If no overflow occurs:
  data_i is added to current hash
  valid_o is asserted
If overflow occurs:
  Addition still happens
  valid_o is deasserted immediately
  One clock cycle is spent in a fix state
Fix Operation:
hash = (hash mod 997) + 7

## Slide 7: FSM Constraints
Must use 2-always block FSM template
  One sequential block
  One combinational block
Reset must be asynchronous and active-low
FSM must contain 4 states:
  start
  idle
  run
  fix
State transitions must follow the given FSM diagram.

## Slide 8: Verification & Part 2 Task
Verification:
  Expected waveform is provided
  Use waveform viewer to verify:
    State transitions
    Hash updates
    Overflow and fix behavior
Part 2 – Collision Analysis:
  Modify the testbench to create a hash collision
  A collision occurs when:
    Two different input sequences produce the same hash
  Use:
    Long input sequences
    Reset between hash operations

## Slide 9: Expected waveform
Assume inputs are 8’d231 (8’hE7)

## Slide 10: Deliverables
Submit a zip file named:
  Lab3_StudentID.zip
Zip file should contain.
  Verilog module file (lab3.v)
  Screenshot of successful simulation
  Waveform screenshot showing correct behavior
  Brief description of router working flow (in your own words)

## Slide 11
Thank you!