## Slide 1
LAB 4 – AES Simulation
IAS0630 Hardware Security SPRING, 2026.
Sharjeel Imtiaz Email: sharjeel.imtiaz@taltech.ee
Centre for Dependable Computing Systems
Dpt. of Computer Systems - School of IT
Tallinn University of Technology
Notes: Started in dec.

## Slide 2: Lab 4 Overview
Objectives:
  Learn to simulate an AES cipher core in Verilog
  Write a testbench to perform multiple encryptions under the same key
  Analyze timing, confusion and diffusion properties via simulation
Tools Used:
  Linux Terminal
  Cadence Xcelium (xrun)
  Verilog HDL
Required Environment:
  Linux OS (lab PCs are dual-boot)
  TalTech credentials for login
  Terminal access
Important Notes:
  If the machine boots into Windows, restart and select Linux
  All work should be done inside your home directory
All Lab Files
  Index of /~spagliar/teaching/ias0630/labs

## Slide 3: Basic Linux Setup
Open a terminal and type.
  cd ~
  mkdir work
  cd work
Load Cadence tools:
  Type Cad
  Select option 1 – Cadence
Download sample design:
  wget https://ati.ttu.ee/~spagliar/teaching/ias0630/labs/sample.v
Run simulation:
  xrun sample.v
Expected Output:
  IAS0630 FSM SAMPLE
  Simulation complete via finish.
Simulate with GUI:
  xrun -gui -debug sample.v
You should observe:
  A waveform window &A counter counting from 32 down to 0

## Slide 4: Lab Description
Task:
  Write a testbench that encrypts 5 different plaintexts using the same AES key.
  For each plaintext, observe done and capture text_out.
  Verify the results using an external AES calculator (suggested: the AES calculator referenced in class).
Questions to answer in your brief report:
  How many cycles does each encryption take?
  Does computation time depend on key or plaintext?
  Can you demonstrate confusion? (show differing outputs for small key/plaintext changes)
  Can you demonstrate diffusion? (small plaintext change affects many output bits)
Source code (starter): aes.zip (top-level aes_cipher_top.v). See lab sources

## Slide 5: Module Interface & Signals
Top-level signals (aes_cipher_top.v):
  clk — clock
  rst_n — asynchronous active-low reset
  ld — load: 1 to load key/text, 0 to perform computation
  key — key input (bus width per top module)
  text_in — plaintext input
  done — indicates encryption finished
  text_out — cipher output
Notes:
  ld = 1 indicates loading inputs; ld = 0 starts computation.

## Slide 6: Activity Instructions
Unzip aes.zip into your working folder and open aes_cipher_top.v.
Create a testbench lab4_tb.v that:
  Applies reset, then releases it.
  Loads a single key (same key for all tests).
  For each of 5 plaintexts:
    Assert ld = 1 and present key and text_in for the required cycles to load.
    Deassert ld (set ld = 0) to start computation.
    Wait for done to assert; record text_out and cycle count.
    Insert a small gap or reset between tests if needed.
  Print runtime info (start cycle, done cycle, cycles taken, text_out).
Verify each text_out against an AES reference (web calculator or trusted tool).
Produce waveform screenshots showing ld, done, text_in, text_out, and key lines.

## Slide 7: Functional Requirements & Verification
Functional Requirements:
  Testbench must preserve a single fixed key across all 5 encryptions
  For each test: measure cycles from start (ld release) to done assertion
  Do not modify core source files; only add a testbench
  Ensure reset is asserted initially and is released before test vectors
Verification:
  Verify outputs using the online AES calculator (or a reference AES tool)
  Show waveforms for at least two tests (one demonstrating typical run, one demonstrating any observable latency or behavior)
  Answer confusion/diffusion questions with concrete examples (e.g., flip 1 bit of plaintext → show output bits changed)

## Slide 8: Deliverables
Submit a zip file named:
  Lab4_StudentID.zip
Zip file should contain.
  Testbench file lab4_tb.v
  Any small scripts you used to generate vectors (optional)
  Screenshots:
    Waveform showing ld, done, text_in, text_out
    Screenshot showing verification result from AES calculator for at least two plaintexts
  Short report (1 page max) containing:
    Key used, list of 5 plaintexts and corresponding ciphertexts
    Cycles taken for each encryption
    Answers to confusion/diffusion questions

## Slide 9
Thank you!