## Slide 1
LAB 5 – Multi-Round Caesar Cipher
IAS0630 Hardware Security SPRING, 2026.
Sharjeel Imtiaz Email: sharjeel.imtiaz@taltech.ee
Centre for Dependable Computing Systems
Dpt. of Computer Systems - School of IT
Tallinn University of Technology
Notes: Started in dec.

## Slide 2: Lab 5 Overview
Objectives:
  Implement a multi-round Caesar-like cipher in Verilog
  Use FSM-based control for multi-cycle computation
  Understand key scheduling and round-based encryption
  Verify encryption timing and correctness using simulation
Tools Used:
  Linux Terminal
  Cadence Xcelium (xrun -gui)
  Verilog HDL
Required Environment:
  Linux OS (lab PCs are dual-boot)
  TalTech credentials for login
  Terminal access
Important Notes:
  If the machine boots into Windows, restart and select Linux
  All work should be done inside your home directory
All Lab Files
  Index of /~spagliar/teaching/ias0630/labs

## Slide 3: Basic Linux Setup
Open a terminal and type.
  cd ~
  mkdir work
  cd work
Load Cadence tools:
  Type Cad
  Select option 1 – Cadence
Download sample design:
  wget https://ati.ttu.ee/~spagliar/teaching/ias0630/labs/sample.v
Run simulation:
  xrun sample.v
Expected Output:
  IAS0630 FSM SAMPLE
  Simulation complete via finish.
Simulate with GUI:
  xrun -gui -debug sample.v
You should observe:
  A waveform window &A counter counting from 32 down to 0

## Slide 4: Lab Description
Task:
  Design a multi-round Caesar-like cipher that encrypts a fixed-length plaintext using a round-dependent key schedule.
Cipher Properties:
  Number of rounds: 4 (fixed)
  Plaintext length: 10 symbols
  Each symbol width: 5 bits
  Total plaintext width: 50 bits

## Slide 5: Key Schedule & Inputs
Key Schedule:
Key width: 20 bits
5 bits per round
  key[4:0] → Round 1 shift
  key[9:5] → Round 2 shift
  key[14:10] → Round 3 shift
  key[19:15] → Round 4 shift
Inputs:
  clk – system clock
  rst_n – asynchronous active-low reset
  ld – indicates inputs are ready to be loaded
  key – round key schedule
  plaintext – input text
Outputs:
  ciphertext – encrypted output
  done – asserted for one clock cycle only

## Slide 6: Functional, Timing Constraints & Guidlines
Must use an FSM (refer to Lab 3)
Entire computation (from ld to done) takes exactly 5 clock cycles
Inputs must be stored internally when ld = 1
done must be asserted for one cycle only
After being done, the design must be ready for new data
Suggested FSM States:
  IDLE – wait for ld
  LOAD – store plaintext and key
  ROUND – perform 4 Caesar rounds
  DONE – assert done for one cycle
Implementation Rules:
  Use 2-always FSM template
    Sequential block for state and registers
    Combinational block for next-state logic
  Cipher shifts are applied round-by-round

## Slide 7: Verification
Expected waveform is provided
Use Xcelium GUI to observe:
  FSM state transitions
  Round counter
  Ciphertext updates
  done pulse timing
Refer to lab5_tb.v to understand stimulus behavior and timing.

## Slide 8: Deliverables
Submit a zip file named:
  Lab5_StudentID.zip
Zip file should contain.
  Verilog module file (lab5.v)
  Screenshot of successful simulation
  Waveform screenshot showing:
    ld, ciphertext, done
  Brief explanation of:
    FSM operation
    Round-based encryption flow

## Slide 9
Thank you!