## Slide 1
LAB 6 – Oscillators and Random Number Generators
IAS0630 Hardware Security SPRING, 2026.
Sharjeel Imtiaz Email: sharjeel.imtiaz@taltech.ee
Centre for Dependable Computing Systems
Dpt. of Computer Systems - School of IT
Tallinn University of Technology
Notes: Started in dec.

## Slide 2: Lab 6 Overview
Objectives:
  Understand hardware oscillators and their behavior
  Design a simple ring oscillator using basic logic components
  Implement a Linear Feedback Shift Register (LFSR)
  Analyze pseudo-random number generation using simulation
Tools Used:
  Linux Terminal
  Cadence Xcelium (xrun -gui)
  Verilog HDL
Required Environment:
  Linux OS (lab PCs are dual-boot)
  TalTech credentials for login
  Terminal access
Important Notes:
  If the machine boots into Windows, restart and select Linux
  All work should be done inside your home directory
All Lab Files
  Index of /~spagliar/teaching/ias0630/labs

## Slide 3: Basic Linux Setup
Open a terminal and type.
  cd ~
  mkdir work
  cd work
Load Cadence tools:
  Type Cad
  Select option 1 – Cadence
Download sample design:
  wget https://ati.ttu.ee/~spagliar/teaching/ias0630/labs/sample.v
Run simulation:
  xrun sample.v
Expected Output:
  IAS0630 FSM SAMPLE
  Simulation complete via finish.
Simulate with GUI:
  xrun -gui -debug sample.v
You should observe:
  A waveform window &A counter counting from 32 down to 0

## Slide 4: Lab Description
Task:
  Design a simple 3-stage ring oscillator using basic logic components.
Design Requirements:
Use the provided components:
  lab6_inv.v (inverter)
  lab6_nand.v (2-input NAND)
The oscillator must have:
  One enable input
  One feedback output
Notes:
  A testbench is not provided
  Students must write a simple testbench
  Goal: measure the oscillation period

## Slide 5: Part 1 – Verification
Verification Tasks:
Enable the oscillator
Observe oscillating output using waveform viewer
Measure:
  Oscillation period
  Stability over time
Hint:
Use waveform cursors in Xcelium GUI to measure period

## Slide 6: Part 2: LFSR-Based RNG
Task: Design a 5-bit Linear Feedback Shift Register (LFSR) with a load capability.
Design Requirements:
Code LFSR directly in RTL (do not use components)
Include:
  clk
  load
  load_data
Use the minimum number of taps
Refer to lecture slide on LFSR taps

## Slide 7: Part 2: LFSR-Based RNG
Functional Requirements
  When load = 1, LFSR loads load_data
  When load = 0, LFSR shifts every clock cycle
  LFSR must generate the full:
    (2⁵ − 1) = 31 unique non-zero states
  Sequence must repeat after full cycle
Verification Tasks:
  Simulate the LFSR over multiple cycles
  Show the complete 31-state sequence
  Verify no early repetition
  Use waveform viewer to demonstrate randomness

## Slide 8: Deliverables
Submit a zip file named:
  Lab6_StudentID.zip
Zip file should contain.
  Verilog file for ring oscillator
  Verilog file for LFSR
  Testbench(s) used
  Screenshot of oscillator waveform (with measured period)
  Screenshot showing full LFSR sequence
  Brief explanation of:
    Oscillator behavior
    LFSR tap selection and sequence length

## Slide 9
Thank you!